## Slide 1: PHY1013S
Gregor Leigh gregor.leigh@uct.ac.za
POTENTIAL DIFFERENCE, CURRENT, RESISTANCE and POWER

## Slide 2: POTENTIAL DIFFERENCE, CURRENT, RESISTANCE and POWER
Learning outcomes: At the end of this chapter you should be able to…
    Model the movement of charge and energy through a conductor as a consequence of a potential difference.
    Relate the current strength in a conductor to the potential difference across it and its own specific features (i.e. length, cross-sectional area, and resistivity).
    Apply the law of conservation of current.
    Calculate power dissipation in circuit elements.

## Slide 3: SOURCES OF (ELECTRICAL) POTENTIAL (DIFFERENCE)
  In an electric field, a potential difference is achieved by the separation of positive and negative charges.
  To maintain this potential difference (and the resultant movement of charged particles), a steady supply of energy is required to continuously separate the charge.
  cell / battery
  (chemical energy)
  generator
  (mechanical energy)
  solar panel / photovoltaic cell
  (light energy)

## Slide 4: POTENTIAL DIFFERENCE and THE TRANSPORT OF ENERGY
  A natural consequence of providing a pathway between two points of different potential in a field is that an object responsive to that type of field (and free to respond) will move from the point of higher potential to the point of lower potential*, taking its energy with it.
  * Unless, of course, the object is a negatively charged particle in an electric field, in which case it is compelled to move from the point of lower potential to the higher.
Supplied energy…
…raises the potential of point A (w.r.t pt B)…
B
A
…creates a potential difference between points A and B…
…causing mass to move…
…and deliver its energy elsewhere.
(by separating masses)

## Slide 5: ELECTRIC CURRENT
  The movement of mobile charges through a conductor (in response to a non-zero field, or potential difference) is called an electric current, or just a current.
  Electric current is a net flow of charge through a material (or device/component made from that material) across which a potential difference is maintained.
  While the actual movement of charge is invisible, we can observe, analyse and make use of its various effects:
    Heating (and lighting);
    Magnetic effects.

## Slide 6: CHARGE CARRIERS
  The mobile charged particles which carry energy from one point in a field to another are called charge carriers.
Material | Charge carriers
conductor
electrolyte
semiconductor
electrons
ions: cations  anions 
electrons  “holes” 

## Slide 7: CURRENT STRENGTH
  Electrons in metals are in continual motion, moving about randomly at speeds of 106 m/s in a delocalised “sea of electrons”.
  Current occurs only when an electric field is established in the metal and the entire “sea” is made to drift in one direction – at a speed of 10–4 m/s (qv).
  Current strength is a measure of the rate of flow of charge through any cross section of conductor:
  Units: [C/s = ampere, A]
V
I
–
+
I

## Slide 8: CURRENT STRENGTH
  Typical household values of current strength:
device | current strength
100 W light bulb | 0.42 A
hairdryer, kettle | 10 A
car starter motor | 200 A
stereo sound system, TV | a few milliamperes
computer | a few nanoamperes

## Slide 9: CONVENTIONAL CURRENT
  Current strength, I, is a scalar, but it does have an associated direction – the direction in which positive charge carriers would move (if they were free to do so).
  Whether we consider electron current or conventional current, the net result in both cases is a movement of positive charges in the direction of the electric field.
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
  For a steady current, I, the amount of charge delivered in a time interval, t, is given by:

## Slide 10: CURRENT DENSITY
I
A
  To describe the flow of charge at a particular point in a conductor we introduce the current density vector .
  For a current I uniformly distributed over a cross sectional area A, the magnitude of is given by:
  points in the same direction as at that point.
  Units: [A/m2]
  For any cross sectional area (of area elements ) in a conductor, the total current is given by:
  (Cf: )
I

## Slide 11: DRIFT SPEED
  The charge in the given section, length L, cross sectional area A, containing n charge carriers per unit volume is .
  and the time taken for this charge to drift out of the volume at drift speed vd (and be replaced by an equal amount drifting in) is
  Hence:
  or :
  where ne is the (mobile) charge density, in [C/m3].
I
A
L

## Slide 12: POWER IN ELECTRIC CIRCUITS
I
  A battery drives a current I through some unspecified device (e.g. a light bulb, a re-chargeable battery, a motor, etc).
  During a time interval dt, a charge dQ = I dt moves from terminal a to terminal b through a decrease in electric potential of Vab = Va – Vb.
  The energy transferred to the device is thus:
  dU = dQVab = I Vab dt ,
  and the rate of energy transfer (i.e. power) is
Va
Vb
a
b
I
I
I
?

## Slide 13: POWER IN ELECTRIC CIRCUITS
Va
Vb
a
b
?
If the device is a … | the energy is transferred …
motor
rechargeable battery
resistor
as work on the motor’s load
to stored chemical energy
to internal thermal energy
  Units: [V A = (J/C)(C/s) = …
… = J/s = watt, W]
I
I
I
I

## Slide 14: ELECTRICAL ENERGY
  From dU = Pdt it can be seen that the standard unit of energy, the joule, is equivalent to a watt second.
  However, considering that about half a million joules of energy are required just to “boil a kettle”, it is more practical for supply companies like Eskom to sell electrical energy by the kilowatt hour:
  1 kilowatt hour = 1 000 W  3 600 s = 3.6  106 J
  The South African “electricity” tariff is currently 37c/kW h.
54c
73c
91c
July 2008
R1.35c
R1.50c

## Slide 15: OHM'S LAW Part I
  “The current through a device is directly proportional to the potential difference applied across it.”
  Some devices show a linear dependence of the current strength I on the applied potential difference V over a wide range of V.
+2
–2
–4
0
+2
+4
potential difference (V)
current strength (mA)
0
–2
1 000  resistor
+4
–2
–4
0
+2
+4
potential difference (V)
current strength (mA)
0
+2
p-n junction diode
  Others do not …

## Slide 16: RESISTANCE
  The same potential difference applied across different conductors will result in different current strengths …
  The resistance of a conductor is defined in terms of the potential difference across it & the current strength in it:
  Units: [V/A = ohm, ]
  It is preferable, however, to see current strength as a consequence of potential difference and resistance:

## Slide 17: THE POTENTIOMETER
  V = IR
V
I
= I
R
  By increasing or decreasing the amount of resistance across which the light bulb is connected, the potentiometer controls the potential difference across the bulb (and thus also its brightness).

## Slide 18: FACTORS AFFECTING RESISTANCE
  The resistance of a conductor depends on its …
    length (R  L)
    cross-sectional area (R  1/A)
    material (R  )
    temperature (R increases in a complex way with temperature – but only for metals …)
  Hence:

## Slide 19: RESISTIVITY
  Since …
  Resistivity, , is defined by:
  Units:
  Since is parallel to we can write
  The inverse of resistivity is conductivity,  :
  Units: [mhos per metre]
  (Seriously)

## Slide 20: OHM'S LAW Part II
  A conducting device is said to obey Ohm's law if its resistance between any two points is independent of the magnitude and polarity of the potential difference between the two points.
  A conducting material is said to obey Ohm's law if its resistivity is independent of the magnitude and direction of the applied electric field.
  ALL materials obey Ohm's law for some particular range of field strengths.
  In all materials, for very large electric fields, Ohm's law no longer applies.

## Slide 21: RESISTIVE DISSIPATION OF POWER
  Electrons moving at constant drift speed through a resistor (or any purely resistive device such as a heater or a toaster) lose their electric potential energy by
  colliding with the molecules in the resistor, causing them to vibrate faster – i.e. the resistor gets hotter.
  Mechanical energy converted to thermal energy is dissipated (lost), since the transfer cannot be reversed.
  Cf…
    motors: work done on the load can be “rewon”
    “recharging” cells: stored chemical energy …
Va
Vb
I
I
I
I

## Slide 22: RESISTIVE DISSIPATION OF POWER
  For resistors (ONLY!) we can combine P = IVab with Ohm’s law (V = IR) to obtain
  and
  Units: [V A = (J/C)(C/s) = J/s = watt, W]
  P = I2R
Va
Vb
I
I
I
I

## Slide 23: POTENTIAL DIFFERENCE, CURRENT and RESISTANCE
  A battery is a source of potential difference, Vbat.
  The battery establishes a potential difference Vwire = Vbat between the ends of a wire.
  The potential difference Vwire causes an electric field E = Vwire/L in the wire.
  The electric field establishes a current I = JA = AE in the wire.
  The magnitude of the current is determined jointly by the battery’s potential difference and the wire’s resistance, according to: